HNAP Development Kit (HDK)
Version 1.2.2

August, 2009

Copyright Notice
Copyright © 2002-2009
Cisco Systems, Inc.
1201 3rd Avenue, Suite 900
Seattle, WA 98101, U.S.A.
All rights reserved.
Contents

# Introduction
The HNAP Development Kit (HDK) is a tool set and source code for generating optimal HNAP server and client code. HNAP methods are specified using the HNAP Specification Language (HSL). The HDK tools generate source code directly from the HSL. Additional HNAP methods and extension methods may easily be added with additional HSL. The HDK also contains an Abstract Device Implementation (ADI) which provides reference implementations of many HNAP methods that can quickly be integrated into any device. The following diagram shows the expected usage flow of the HDK components.

+
+
 Device Glue
 HNAP Implementation
 ADI Glue

HDK ADI
HDK Core

Device Integration
 ADI Source
 HDK Core Source
 C Server Code
 HDK HSL

The HDK contents are intended to be used unmodified. You should build source files and include headers directly out of your HDK directory in your source code. The next section details the contents of the HDK directory tree.
## HDK Benefits
The HDK was designed to provide a high-quality, small-footprint HNAP implementation with minimal device integration cost. Here are some benefits of using the HDK.
- High-quality HNAP implementation. The HDK was designed for quality from the ground up. Repetitive and error-prone tasks such as XML serialization and de-serialization have been abstracted away by using code generation tools and a simple structure API. It contains an extensive unit test framework that ensures correct responses to an extensive set of test cases. The unit test framework also ensures that there are no memory leaks.
- Small device footprint. The HDK was designed to require minimal size in the device firmware. This is accomplished by maximizing code re-use through code generation and the HDK’s simple, regular structure API.
- Quick device integration. Integrating the HDK into your device is quick and easy. The HDK provides sample applications as a starting point for your HDK integration.
- Faster HNAP development. The HNAP Specification Language (HSL) and the HDK’s code generation tools allow you to quickly add new HNAP extension methods. Simply add the HSL for your new method and recompile. The HDK generates a callback stub which is available in your device.
- High-quality Abstract Device Implementation. The HDK ships with a well tested Abstract Device Implementation (ADI) for several of the HNAP 1.2 specifications. To integrate the ADI into your device you implement three simple “ADI Glue” functions (HDK_Device_GetValue, HDK_Device_SetValue, and HDK_Device_ValidateValue).
## Setup on Ubuntu Linux
To build and run the HDK unit tests and samples on Ubuntu Linux you must first configure your system properly. Execute the following commands from a terminal window:
sudo apt-get update
sudo apt-get install build-essential
sudo apt-get install libexpat1-dev
sudo apt-get install libxml2-dev
To run unit tests execute the runtests.py script from the unittest directory.
./runtests.py
## Setup on Windows
To build and run the HDK unit tests and samples on Windows XP (and later) you must first configure your system properly. The following tools are required:
Python 2.x – http://www.python.org/download/releases/
Expat 2.0.x – http://sourceforge.net/project/showfiles.php?group_id=10127
To run unit tests execute the runtests.py script from the unittest directory.
vsvars.bat
python runtests.py
## Setup on OS X
To build and run the HDK unit tests on OS X you must first install Xcode on your system.
http://developer.apple.com/TOOLS/Xcode/
To run unit tests execute the runtests.py script from the unittest directory.
./runtests.py
## HDK Contents
+---doc
| hdk.pdf	This document
|
+---hnap	HNAP 1.2 HSL source directory
|
+---sample
| \---cgi	CGI sample integration
| \---hnapd	Stand-alone HTTP server sample integration
| \
|
+---src	HDK Core source code directory
| hdk.c	HDK request handler
| hdk.h	HDK request handler header
| hdk_adi.c	HDK ADI
| hdk_adi.h	HDK ADI header
| hdk_encode.c	HDK encoding utilities
| hdk_encode.h	HDK encoding utilities header
| hdk_interface.h	HDK Device Glue header
| hdk_internal.h	HDK internal header – DO NOT INCLUDE
|
+---tools
| hnapgen.py	HSL parser and code generation tool
| hnappost.py	HNAP POST request test tool
|
\---unittest	HDK unit test framework
   | runtests.py	HDK unit test application
# HDK Sample Applications
The sample applications provided by the HDK are designed to be the starting point for your HDK integration.
## The CGI Sample (cgi)
The Common Gateway Interface (CGI) web application interface is supported by a wide variety of web servers. If you already have a web server on your device such as lighttpd or Cherokee this is a good HDK integration choice.
The CGI sample application is located in the sample/cgi directory. It contains the following files:
hdk_cgi.c	CGI application main entry point
hdk_context.c	HDK context implementation
hdk_context.h	HDK context definition
hdk_device.c	HDK and ADI device glue function implementations
hdk_methods.c	HDK action function implementations
Makefile	Linux Makefile
Makefile.nmake	Windows Makefile
README.txt	Readme file
To get started with a CGI integration copy all of the sample files (except perhaps README.txt and Makefile.nmake) to a directory in your device source tree and integrate the makefile with your build system.
You should install the application in the /HNAP1/ directory of your web server. Ensure that it is configured to be the default page of the /HNAP1/ directory and that it is handled by the web server's CGI handler.
### FastCGI
The CGI sample also supports the FastCGI web application interface. FastCGI has the benefit of being considerably faster than CGI. To use FastCGI define the HDK_FCGI preprocessor macro on your compiler's command line in your makefile.
## The Stand-Alone Server Sample (hnapd)
If your device does not have an HTTP server, the stand-alone HNAP server sample may provide the right integration method for your device. The sample contains the following files:
hnapd.c	Stand-alone HNAP server application
hdk_context.c	HDK context implementation
hdk_context.h	HDK context definition
hdk_device.c	HDK and ADI device glue function implementations
hdk_methods.c	HDK action function implementations
Makefile	Linux Makefile
To get started with a stand-alone server integration copy all of the sample files to a directory in your device source tree and integrate the makefile with your build system.
You will need to ensure that the hnapd application is run at system startup time.
# HDK Device Integration
There are two steps to integrating the HDK into your device firmware. First, call the HDK's HDK_IsHNAPRequest, HDK_RequiresAuth, and HDK_HandleRequest functions (defined in src/hdk.h) from your HTTP server. Second, you need to implement the "device glue" functions.
## Detecting HNAP Requests
If you are integrating the HDK using a web server module or if you are directly integrating with your web server, you may need to determine whether a request is an HNAP request. To do this, call the HDK_IsHNAPRequest prior to authenticating and handling the request. HDK_IsHNAPRequest returns non-zero if this is an HNAP request.
extern int HDK_IsHNAPRequest(char* pszPath);
## HTTP Authentication
To determine if the HNAP request requires authentication, call the HDK_RequiresAuth function prior to authenticating the request. If HDK_RequiresAuth returns non-zero your HDK application should verify the HTTP basic authentication. If HDK_RequiresAuth returns zero then your HDK application should allow the request without checking HTTP basic authentication.
extern int HDK_RequiresAuth(int fGet, char* pszSoapAction);
## HDK Request Handler
HDK_HandleRequest is the main entry point for handling an HNAP request. Here is its definition:
extern HDK_Enum_Result HDK_HandleRequest(void* pDeviceCtx, int fGet,
   unsigned int cbContentLength, char* pszSoapAction);
The first argument, pDeviceCtx, is called the device context. This is a void pointer to any data you need to implement any aspect of the HDK integration. Typically, this will be a struct containing FILE handles for input/output streaming or result state to act on outside the HDK request handling, such as the need to reboot the device.
The second argument, fGet, should be set to 1 if this is an HTTP GET request. If it is 0 it is handled as a POST request.
The third and fourth arguments, cbContentLength and pszSoapAction, correspond to the HTTP headers Content-Length and SOAPAction, respectively.
## HDK Device Glue Functions
The HDK "device glue" is comprised of three simple functions that you implement which allow the HDK to read request data and write response data. The function prototypes are defined in src/hdk_interface.h.
/* Request input stream */
extern int HDK_Device_Read(void* pDeviceCtx, char* pBuf, int cbBuf);
/* Prepare the response output stream for writing */
extern void HDK_Device_PrepareWrite(void* pDeviceCtx,
   HDK_Enum_Result* pResult);
/* Response output stream */
extern void HDK_Device_Write(void* pDeviceCtx, char* pBuf, int cbBuf);
HDK_Device_Read reads the requested number of bytes (cbBuf) from the request into a buffer (pBuf). It returns the number of bytes actually read. HDK_Device_Read should return less-than or equal-to zero when no more data can be read.
HDK_Device_PrepareWrite is used to do anything needed to prepare the device for the HNAP response. Depending on the type of integration this may involve flushing the socket of input bytes. The pResult argument is an in/out parameter that allows you to modify an “OK” result to a “REBOOT” if your device requires a reboot as the result of a request.
HDK_Device_Write writes the requested number of bytes (cbBuf) from a buffer (pBuf).
## HDK Preprocessor Macros
The HDK optionally makes use of the following preprocessor macros. Define these on your compiler's command line in your makefile if you need to change the default behavior.
HDK_LIBXML2 – The HDK_LIBXML2 preprocessor macro tells the HDK to use libxml2 for XML parsing. Libxml2 is only supported on the Linux platform. The default XML parser is the Expat XML parser.
HDK_CGI – Define the HDK_CGI preprocessor macro if you are using the CGI or FastCGI web application interface.
HDK_MAX_ELEMENTS – The maximum number of elements allowed in a client request. If the maximum is exceeded parsing is stopped and a client soap error is returned. The default value is 1024.
HDK_MAX_VALUESIZE – The maximum size of an XML element's value text. If the maximum is exceeded parsing is stopped and a client soap error is returned. The default value is 16K.
HDK_MAX_TOTALVALUESIZE – The maximum total value size for a client request. If the maximum is exceeded parsing is stopped and a client soap error is returned. The default value is 64K.
# Abstract Device Implementation (ADI) Integration
The HDK contains an Abstract Device Implementation (ADI) for the following HNAP 1.2 specifications:
- HNAP 1.2 Core
- HNAP 1.2 Router
- HNAP 1.2 Wireless Client
By implementing the three "ADI glue" functions defined in src/hdk_adi.h and compiling and linking with the ADI implementation, src/hdk_adi.c, you will have a fully functional HNAP 1.2 implementation.
The ADI glue API works with the HDK structure API to provide a pure device abstraction. The three functions that you must implement are HDK_Device_GetValue, HDK_Device_SetValue, and HDK_Device_ValidateValue. The function prototypes are defined in src/hdk_adi.h.
int HDK_Device_GetValue(void* pDeviceCtx,
   HDK_Struct* pStruct, HDK_DeviceValue eValue,
   HDK_Struct* pInput);
int HDK_Device_SetValue(void* pDeviceCtx,
   HDK_DeviceValue eValue, HDK_Struct* pStruct);
int HDK_Device_ValidateValue(void* pDeviceCtx,
   HDK_DeviceValue eValue, HDK_Struct* pStruct);
HDK_Device_GetValue gets an abstract device value as defined by the HDK_DeviceValue enumeration defined in src/hdk_adi.h. The first argument is the device context (pDeviceCtx). The second argument is the struct into which the device value is to be retrieved. The third argument is the device value to be retrieved. The fourth argument, pInput, is a struct containing any input arguments for the get. This is used for indexed get values such as those required by GetWLanRadioSettings where a radio ID must be specified. Return 1 for success and 0 for failure.
HDK_Device_SetValue sets an abstract device value. The first argument is the device context (pDeviceCtx). The second argument is the device value to be set. The third argument is the struct containing the members to set to the device. Return 1 for success and 0 for failure.
HDK_Device_ValidateValue is used to validate a device value prior to a call to HDK_Device_SetValue. Return 1 for success (the device value is valid to set) and 0 for failure.
The comments above each device value enumeration value define which member elements and types should be get/set. For example, HDK_DeviceValue_VendorName specifies that it should set HDK_Element_VendorName element with type string to the output struct. Refer to src/hdk_adi.c to determine which HDK_DeviceValue enumeration values are used for get and/or set.
# HNAP Specification Language (HSL)
The HNAP Specification Language (HSL) is a simple language designed to concisely define HNAP structures and methods for use in generating server and client code. HSL allows you to define three basic HNAP entities: actions, structures, and enumerations. Here’s an example:
# A documentation section
#@@ h3 My HNAP
#@ Getter and setter actions for my settings.
#@ The array must have no more than ten items.
#@@ end
# A namespace declaration
namespace "http://mydomain.com/HNAPExt/"
# An enumeration definition
#@ MyEnum represents two values.
enum MyEnum
"MyValue1" #@ The first value.
"MyValue2" #@ The second value.
# A structure definition
#@ MyStruct is a collection of stuff.
struct MyStruct
int IntMember #@ The integer
string StringMember #@ The string
IPAddress IPAddressMember #@ The IP address
# A "setter" action definition
#@ MySetAction sets something.
action MySetAction
input
#@ The new value.
MyStruct[] MyStructArray #@ No more than ten items
# A "getter" action definition
#@ MyGetAction gets something.
action MyGetAction
output
MyStruct[] MyStructArray #@ The current value.
## Comments and Documentation
Comments begin with '#' and continue to the end of the line.
Documentation comments are comments that begin with '#@'. They can be found in two places, in documentation sections, and attached to HSL objects.
Documentation comments may contain XHTML, and tags must be in lower case. The hdkdocs.py tool will wrap text in “p” tags if necessary, and insert omitted end tags so as to generate valid XHTML. These element types are allowed:
- all inline (text-level) elements (recommended: br, q, b, i, em, strong, tt, var, a, img)
- these block-level (and other) elements: p, table, tr, td, th, ul, ol, li
An empty '#@' line will generate a paragraph break. Otherwise, successive '#@' lines will end up on a single line. Use '<br />' to generate a line break.
### Documentation Sections
Documentation sections begin with a line of the form '#@@ <type> <title>' and end with the line '#@@ end'. In between it contains documentation comments. For instance:
#@@ h3 My HNAP
#@ Getter and setter actions for my settings.
#@ The array must have no more than ten items.
#@@ end
Here the type of the section is 'h3', and the title is 'My HNAP'. The contents of the section is the documentation from the two lines within.
The contents of a section is optional. The '#@@ end' can be omitted if it is followed by another documentation section. These are the supported documentation section types:
h1, h2, h3, h4:	This kind of section will be shown underneath the specified level of header.
date:	The title of this section is the date of the specification. It will be shown on the front page. The contents will be ignored.
version:	The title of this section is the version of the specification. It will be shown on the front page. The contents will be ignored.
top:	The contents will be placed at the top of the document.
title:	The title of this section is the title of the specification. It will be shown on the front page. The contents will be ignored.
abstract	An abstract of the specification. It will be shown on the front page.
copyright	A copyright notice. It will be shown on the front page.
### Object Documentation
Documentation can be attached to types, structure members, enumeration values, actions, action members and return values, simply by putting documentation comments before the object, or after the object on the same line. For example:
#@ MySetAction sets something.
action MySetAction
input
#@ The new value.
MyStruct[] MyStructArray #@ No more than ten items
Here both MySetAction and its MyStructArray parameter have documentation attached.
### Inline Images
The hdkdocs.py tool can import images and include them inline in the file as base64-encoded “data:” URLs, using an '@' symbol in the 'src' attribute.
#@ <img src="@images/myimage.png" alt="My Image" />
The tool will substitute the contents of the image file, with base64 encoding.
### HTML Layout
Generated HTML files are structured like this:
- A front page, consisting of:
  - The contents of the 'top' section, if any
  - The title “Home Network Administration Protocol (HNAP) for <title>”, where <title> is the title of the “title” section.
  - Version, date, abstract and copyright sections, if present, in that order. Each has its own formatting, controlled by the included style sheet.
- table of contents
- all documentation sections of type h1, h2, h3, h4
- HSL actions
- HSL structures
- HSL enumerations
### Generating HTML
Run the hdkdocs.py tool to generate an HTML specification document from your HSL file, using python.
python hdkdocs.py -o myspec.html myspec.hsl
Specify the output HTML file with the -o flag (here “myspec.html”), and one or more HSL files on the command line. The hdkdocs.py tool will create an HTML file documenting all the actions and types in the HSL files.
## HSL Types
HSL supports nine primitive member types:
Type	Description
int	An integer value as described by http://www.w3.org/TR/xmlschema-2/#integer.
string	A string value as described by http://www.w3.org/TR/xmlschema-2/#string.
blob	A base64 encoded binary "blob" as described by http://www.w3.org/TR/xmlschema-2/#base64Binary.
bool	A boolean value as described by http://www.w3.org/TR/xmlschema-2/#boolean.
long	A long integer value as described by http://www.w3.org/TR/xmlschema-2/#long.
datetime	A dateTime value as described by http://www.w3.org/TR/xmlschema-2/#dateTime.
IPAddress	An IP Address value. For example, "192.168.1.1".
MACAddress	A MAC Address value. For example, "00:1E:E5:38:90:CF".
stream	A streamed string member. Stream types are intended to be used for very large data only. Streams are discussed further in the Server API section.
stream64	A streamed blob member. Stream types are intended to be used for very large data only. Streams are discussed further in the Server API section.

HSL supports array members by appending "[]" to the member type (see example above). Arrays in HSL are always unbounded.
## HSL Actions
HSL actions may contain two optional structure definition sections: input and output. These structures define the input parameters to the HNAP action and the output parameters to the HNAP action, respectively.
The output structure (whether present or not) is always given an implicit result member. In the example above, the two defined actions get result members called "MySetActionResult" and "MyGetActionResult", respectively. This result member receives the HNAP result code (e.g. "OK" or "ERROR").
## HSL Action Results
By default HSL implicitly defines two built-in result codes ("OK” and "ERROR"). The HDK exposes these result codes through the built-in result enumeration type, “result”. HSL actions can define custom error result codes by using the optional result section. For example:
namespace "http://mydomain.com/HNAPExt/"
action MySetAction
input
int a
result
"ERROR_BAD_VALUE"
## Importing HSL Types
HSL structures and enumeration definitions may be imported from other HSL files. This is done using the import statement. For example:
a.hnap
namespace "http://mydomain.com/HNAPExt/"
struct MyStruct
   int a
b.hnap
namespace "http://mydomain.com/HNAPExt/"
import "a.hnap"
action MyAction
   input
       MyStruct m
The import statement will only import structures and enumerations, not actions. Import files are searched for first in the current HSL file's directory and then in the hnapgen.py import path.
## Namespace Abbreviations
Structures and enumerations defined in other namespaces may be used in your namespace. This is done using the namespace abbreviation syntax. For example:
a.hnap
namespace "http://theirdomain.com/HNAPExt/"
struct TheirStruct
   int a
b.hnap
namespace "http://mydomain.com/HNAPExt/"
import "a.hnap"
namespace their "http://theirdomain.com/HNAPExt/"
action MyAction
   input
       their:TheirStruct m
## Attributes
HSL allows the specification of optional attributes on action and member definitions. These attributes are used to imply a non-default behavior of the HNAP entity. Attributes may be a name or a name/value pair. The attribute list is a comma delimited list of attributes surrounded by a pair of matching square brackets. The following subsections describe the available attributes.
### The “noauth” Action Attribute
The “noauth” action attribute tells the HDK server not to require HTTP basic authentication for an action.
[noauth] action MyAction
   output
       int A
### The “array_element” Member Attribute
When you define an array member in HSL an array structure type is automatically created behind the scenes. The array structure type has a single element member. By default this element member is named by the simple type name (e.g. “string” or “int”). The element name is “string” for enumerations and and the struct name for structures. If the default member element name is undesirable, you may use the “array_element” member attribute to override the default:
struct MyStruct
   [array_element=”Number”] int[] MyInts
## Line Continuation Syntax
HSL provides a line continuation syntax for long lines. A line is continued by specifying a backslash (“\”) character at the end of the line. Comments may occur following a line continuation.
[attribute1, \ # A comment
attribute2] \ # Another comment
action MyAction
   input
       int A
# HDK Server API
When you define an action in HSL, hnapgen.py generates a server implementation which will call your method (action) callback function. For example, consider the following HSL:
namespace "http://mydomain.com/HNAPExt/"
action MyAction
   input
       int a
   output
       string b
From this, hnapgen.py generates server code which will call the following method callback when it receives a MyAction request:
void HDK_Method_Mydomain_MyAction(void* pDeviceCtx,
        HDK_Struct* pInput,
        HDK_Struct* pOutput)
{
}
The pDeviceCtx argument is your device's device context. The device context is discussed in the HDK Device Integration section. The pInput argument is the method's input structure. The pOutput argument is the method's output structure.
## Input and Output Struct Validation
The HDK ensures that input structs are valid according to the HSL input struct schema. This protects your method callback from invalid elements, invalid element cardinality, and missing required elements. Schema element order is not enforced. If the HDK request handler receives invalid request XML it will return the following client fault.
<?xml version="1.0" ?>
<soap:Envelope xmlns:soap="http://schemas.xmlsoap.org/soap/envelope/">
<soap:Body>
<soap:Fault>
<faultcode>soap:Client</faultcode>
<faultstring>Invalid request XML</faultstring>
</soap:Fault>
</soap:Body>
</soap:Envelope>
The HDK server also validates output structs. This prevents the server from returning invalid responses to HNAP clients. Schema element order is not enforced. However, the output struct is serialized in schema order thus providing the most consistent output for consumption by HNAP clients. If an HNAP method callback function returns an invalid output struct the following server fault code is returned.
<?xml version="1.0" ?>
<soap:Envelope xmlns:soap="http://schemas.xmlsoap.org/soap/envelope/">
<soap:Body>
<soap:Fault>
<faultcode>soap:Server</faultcode>
<faultstring>Invalid response XML</faultstring>
</soap:Fault>
</soap:Body>
</soap:Envelope>
## Getting Input Struct Member Values
To get an input struct member value use one of the HDK_Get_<Type> functions with the member's element from within your method callback. Element enumeration values are defined in the generated file hdk_data.h. For example, to get the int member value "a" in the example above:
int* pA = HDK_Get_Int(pInput, HDK_Element_Mydomain_a);
HDK_Get_X returns zero if the member does not exist in the struct. Otherwise, it is a pointer to the value. For convenience, an "Ex" form of the get functions is also provided. If the specified member does not exist, the "Ex" form of the get functions returns a default value:
int a = HDK_Get_IntEx(pInput, HDK_Element_Mydomain_a, 0);
## Getting Sub-Structure Member Values
An input struct may also contain other structs. You gain access to sub-structs using the HDK_Get_Struct function:
HDK_Struct* pMyStruct =
 HDK_Get_Struct(pInput, HDK_Element_Mydomain_mystruct);
if (pMyStruct)
{
   int a = HDK_Get_IntEx(pMyStruct, HDK_Element_Mydomain_a, 0);
}
## Getting Array Member Values
Arrays in the server implementation are much like structs. To iterate an array you begin with the struct head and continue until there is no next structure node. To access each array member value is the HDK_Get_<Type>Member functions. Here's an example:
HDK_Member* pMember;
HDK_Struct* pMyArray =
 HDK_Get_Struct(pInput, HDK_Element_Mydomain_myarray);
for (pMember = pMyArray->pHead; pMember; pMember = pMember->pNext)
{
   int* pA = HDK_Get_IntMember(pMember);
   if (pA)
   {
       /* ... */
   }
}
## Setting Output Struct Member Values
To set an output value in the method output struct use one of the HDK_Set_<Type> functions. For example, to set the output string member in the example at the top of this section:
HDK_Set_String(pOutput, HDK_Element_Mydomain_b, "abc");
## Setting Sub-Structure Member Values
Sub-structures are created with the HDK_Set_Struct function. For example:
HDK_Struct* pMyStruct =
 HDK_Set_Struct(pOutput, HDK_Element_Mydomain_mystruct);
if (pMyStruct)
{
   HDK_Set_Int(pMyStruct, HDK_Element_Mydomain_a, 10);
}
## Adding Array Member Values
Arrays in the server implementation are much like structs. To create an array and add values to it use the HDK_Set_Struct function and the HDK_Append_<Type> functions. For example:
HDK_Struct* pMyArray =
 HDK_Set_Struct(pOutput, HDK_Element_Mydomain_myarray);
if (pMyArray)
{
   HDK_Append_Int(pMyStruct, HDK_Element_Mydomain_a, 1);
   HDK_Append_Int(pMyStruct, HDK_Element_Mydomain_a, 2);
   HDK_Append_Int(pMyStruct, HDK_Element_Mydomain_a, 3);
}
## Setting the Method Result
The HNAP result of a method is specified setting the action's result element in the output structure. By default, the result element is set to HDK_Enum_Result_OK. To set an HNAP error (for an action called "MyAction"):
HDK_Set_Result(pOutput, HDK_Element_Mydomain_MyActionResult,
        HDK_Enum_Result_ERROR)
When the result code is set to an HNAP error result code (e.g. any HNAP code beginning with "ERROR_") only the result member is output. Any other structure members which have been added to the output struct are not output.
## Stream Output Members
Occasionally you may need to output large amounts of data from an HNAP method (e.g. DownloadSpeedTest). On these occasions you should use the stream or stream64 HSL member types. To add a stream member from within the member callback function use the HDK_Set_Stream function:
HDK_Set_Stream(pOutput, HDK_Element_Mydomain_s, MyStreamFn);
MyStreamFn is an output member stream callback function that will be called during the serialization process. You define a stream callback function as follows:
static void MyStreamFn(
   void* pDeviceCtx,
   HDK_Struct* pInput,
   void* pMemberCtx,
   void* pStreamCtx,
   HDK_StreamOutFn pfnStreamOut)
{
   pfnStreamOut(pDeviceCtx, pMemberCtx, "abc", 3);
   pfnStreamOut(pDeviceCtx, pMemberCtx, "def", 3);
}
The input structure (pInput) is the same input structure passed to the method callback function.
The HDK_StreamOutFn argument is a streaming output function. Call this with the data you wish to stream out. The HDK_StreamOutFn is responsible for all encoding. The "stream" function will encode XML entities. The "stream64" function will encode your binary stream to base64. You may call the output stream function as many times as you like.
Your output callback function will be called twice during the serialization process. The first time is to compute the content length of the response. The second time is to actually perform the output. Because of this it is critical that the output of your member stream function is consistent across invocations. If it is not, the content length of the output will be incorrect.
## Stream Input Members
Occasionally you may need to provide large amounts of input data to an HNAP method (e.g. FirmwareUpload). For this the HDK provides the stream and stream64 HSL member types. When you define a stream or stream64 member the HDK requires that you to define Open, Value, and Close input stream handler functions. For example:
action MyAction
   input
       stream64 Input
In this example you will need to define the following functions in addition to the HNAP method callback function.
int HDK_Method_MyAction_Input_Open(void* pDeviceCtx)
{
   return 1;
}
int HDK_Method_MyAction_Input_Value(void* pDeviceCtx, char* pBuf,
        unsigned int cbBuf)
{
   return 1;
}
int HDK_Method_MyAction_Input_Close(void* pDeviceCtx)
{
   return 1;
}
These functions are called during XML parsing and provide you streamed access to the decoded input data. The Open function is called on the XML element's open tag, the Value function is called (possibly multiple times) to receive the XML element's value, and the Close function is called on the XML element's close tag. Each function should return 1 to indicate success and 0 to indicate failure.
# HDK Tools
The HDK tools directory contains tools for generating source code and testing HNAP devices.
## hnapgen.py
The hnapgen tool is used to generate C server code and WSDL client code from HSL. Its usage is as follows:
Usage: hnapgen.py [options] hnap...
Options:
 -h, --help show this help message and exit
 -o dir output directory
 -b name base file name (e.g. 'hdk')
 -s generate server code
 --server-methods generate server method implementation file
 --server-capi generate server C API file s
 --server-transactions
        generate server transaction support
 -w generate WSDL
 -i action include only specified HNAP actions
 -x action exclude specified HNAP actions
 -I dir add directory to import path
hnapgen is intended to be integrated in your build process much like you would a compiler. For typical usage see the cgi sample makefile included with the HDK.
To generate source code for a server use the -s option. For example:
./hnapgen.py -s myhnap.hnap
This generates three files which are required for an HDK server:
hdk_data.h	HDK structure API header
hdk_data.c	HDK structure API source
hdk_methods.h	HNAP method callback pre-declarations
The --server-methods switch generates hdk_methods.c file which contains empty implementations of the HNAP method callbacks. You will typically use --server-methods when you are creating your project, if at all.
To exclude actions from your server implementation use the -x switch. For example:
./hnapgen.py -s myhnap.hnap -x MyAction2 -x MyAction3
The former will exclude MyAction2 and MyAction3 from the server implementation while leaving all other actions defined in myhnap.hnap.
The “--server-capi” switch is used to enable the experimental C API feature. The “--server-transactions” switch is used to enable the experimental HNAP transactions feature.
## hnappost.py
The hnappost tool is used to post HNAP actions to a device. Its usage is as follows:
Usage: hnappost.py [options] host
Options:
 -h, --help show this help message and exit
 -u user Host user name
 -p password Host password
 -s Use SSL
 -m method Send simple HNAP request
 -f file Send HNAP request from file
 -t Send Reboot request
 -w file Send FirmwareUpload request
 -b file Send GetConfigBlob request
 -r file Send SetConfigBlob request
 -d Send RestoreFactoryDefaults request
 -o Output request content
For example, to call GetDeviceSettings on the device at 192.168.1.1:
./hnappost.py 192.168.1.1 -u user -p password -m GetDeviceSettings
If you define a simple HNAP getter action in your own extension namespace you can call it as follows:
./hnappost.py 192.168.1.1 -u user -p pass -m http://mydomain.com/Action
You may send more complex requests to the device by using the -f switch.
./hnappost.py 192.168.1.1 -u user -p password -f myaction.request
Where myaction.request is a file of the form:
SOAPAction: "http://mydomain.com/HNAPExt/MyAction"
<?xml version="1.0" encoding="utf-8"?>
<soap:Envelope xmlns:soap="http://schemas.xmlsoap.org/soap/envelope/" soap:encodingStyle="http://schemas.xmlsoap.org/soap/encoding/">
<soap:Body>
<MyAction xmlns="http://mydomain.com/HNAPExt/">
</MyAction>
</soap:Body>
</soap:Envelope>
hnappost also provides commands for easy access to HNAP methods useful in a development environment.
The -t argument sends an HNAP Reboot request.
./hnappost.py 192.168.1.1 -u user -p password -t
The -w argument sends an HNAP FirmwareUpload request with the given file.
./hnappost.py 192.168.1.1 -u user -p password -w code.bin
The -b argument sends an HNAP GetConfigBlob request and saves the configuration blob to the given file:
./hnappost.py 192.168.1.1 -u user -p password -b backup.blob
The -r argument sends an HNAP SetConfigBlob request with the given file:
./hnappost.py 192.168.1.1 -u user -p password -r backup.blob
The -d argument sends an HNAP RestoreFactoryDefaults request.
./hnappost.py 192.168.1.1 -u user -p password -d
# WSDL Generation and Usage
The HDK tools can generate WSDL from HSL for client code. Many programming environments, such as .NET, can use WSDL to generate native code for communicating with your HNAP server methods. To generate WSDL from HSL use hnapgen.py with the -w argument.
hnapgen.py -w myhnap.hnap
This outputs the WSDL to hdk.wsdl. To generate C# code using the WSDL file use the svcutil.exe tool included with the Windows SDK (shown below generating C# code for Visual Studio 2008):
"$(WindowsSdkDir)\bin\svcutil.exe" /t:code /language:csharp
/tcv:Version35 /out:..\client\hdk.cs "$(IntDir)\hdk.wsdl"
# Experimental Features
## HDK C API
The experimental C API feature provides an API for calling HNAP functions locally on the device from C clients. The C API feature is enabled by using the “--server-capi” switch of hnapgen.py in your HDK application's makefile. This will generate two additional files: hdk_capi.h and hdk_capi.c. You should compile and link hdk_capi.c with your HDK shared library. Each C API function takes an HDK device context. Depending on whether the action has input or output parameters in HSL it may take an input HDK_Struct pointer or an output HDK_Struct pointer. Here's an example usage for GetDeviceSettings (in this example a null device context is used).
HDK_Struct output;
if (HDK_SUCCEEDED(HDK_CAPI_PN_GetDeviceSettings(0, &output)))
{
   printf(“The device name is \”%s\”\n”,
        HDK_Get_StringEx(output, HDK_Element_PN_DeviceName, “”));
}
Use the “hidden” action attribute if you want your HNAP action to only be available for use through the C API.
[hidden] action MyAction
## HNAP Transactions
The experimental HNAP transactions feature allows multiple HNAP method calls to be made in a single request. The HNAP transactions feature is enabled by using the “--server-transactions” switch of hnapgen.py in your HDK application's makefile. This will auto-generate the HNAP method and code for handling transactions. The result of a transaction contains the response from each method call. The result of the transaction request is “OK” if all methods succeed or the error code of the first method that fails.
Devices that support transactions must implement a “transacting context”. A transacting context does not persist any state until the device context is freed. Thus, any device values which are modified as part of the transaction must be cached in the device context until the device context is freed. Furthermore, any get of a modified device value should return the modified value (which has yet to be persisted).
Here is an example of an HNAP transaction request:
SOAPAction: http://cisco.com/HNAP/Transaction
<?xml version="1.0" encoding="utf-8"?>
<soap:Envelope xmlns:soap="http://schemas.xmlsoap.org/soap/envelope/">
<soap:Body>
<Transaction xmlns="http://cisco.com/HNAP/">
<RestoreFactoryDefaults xmlns="http://purenetworks.com/HNAP1/">
</RestoreFactoryDefaults>
<SetWLanRadioSettings xmlns="http://purenetworks.com/HNAP1/">
<RadioID>RADIO_2.4GHz</RadioID>
<Enabled>false</Enabled>
<Mode>802.11n</Mode>
<SSID>craig_ut610n</SSID>
<SSIDBroadcast>true</SSIDBroadcast>
<ChannelWidth>0</ChannelWidth>
<Channel>0</Channel>
<SecondaryChannel>0</SecondaryChannel>
<QoS>true</QoS>
</SetWLanRadioSettings>
<SetWLanRadioSettings xmlns="http://purenetworks.com/HNAP1/">
<RadioID>RADIO_5GHz</RadioID>
<Enabled>false</Enabled>
<Mode>802.11n</Mode>
<SSID>craig_ut610n_media</SSID>
<SSIDBroadcast>true</SSIDBroadcast>
<ChannelWidth>0</ChannelWidth>
<Channel>0</Channel>
<SecondaryChannel>0</SecondaryChannel>
<QoS>true</QoS>
</SetWLanRadioSettings>
</Transaction>
</soap:Body>
</soap:Envelope>
You may generate the default implementation for HDK_Method_Transaction by using the hnapgen.py “--server-methods” switch.
## HNAP Services
The experimental HNAP services feature is comprised of two new HNAP methods (defined in hnap/services.hnap) and a new HSL “service” keyword. An HNAP service is a guarantee to clients of the presense of a set of HNAP methods. To define a service in HSL use the service keyword:
action MyAction
action MyAction2
service MyService
   actions
       MyAction
       MyAction2
Now, the “MyService” service is automatically reported by the provided GetServices and GetServiceInfo implementations (see services.hnap). You may control your reported service levels by modifying the implementation of the HDK_Callback_ServiceLevel function:
static int HDK_Callback_ServiceLevel(void* pDeviceCtx,
        HDK_Service service)
You may generate the default implementations for HDK_Callback_ServiceLevel, HDK_Method_GetServices, and HDK_Method_GetServiceInfo by using the hnapgen.py “--server-methods” switch.